## Slide 1
POWERNEXT 2026
TRACK 1
ImpulseTwin AI
Impulse generator settings,
explained and tested
TEAM CR7
Adithya P (Team lead)
Siddhanth K Jain
Kamma Rohan
Dinesh Kulkarni

## Slide 2
PROBLEM AND SOLUTION
The test request and recommendation workflow
Challenge targets: Lightning 1.2 / 50 µs. Switching 250 / 2,500 µs.
02
The right voltage also needs the right pulse shape.
Engineers must meet timing limits with the generator and resistor stock available.
Configure
Crest, impulse type, load and profile.
Check and search
Limits, counted stock and feasible settings.
Simulate
Circuit waveform and charging requirement.
Rank and explain
Stage count, R networks, deviations and alternatives.
Each saved run keeps its settings, assumptions and provenance.

## Slide 3
VERTICAL LAYERS AND TECH STACK
System architecture
1. Presentation
Browser interface
Next.js, React / React DOM, TypeScript, Tailwind CSS
Apache ECharts, Three.js (WebGL), Lucide, Canvas / SVG
2. API & validation
Python application
Python, FastAPI, Starlette, Pydantic, Uvicorn
HTTP/JSON requests and file uploads with python-multipart
3. Engineering
Physics and scoped ML
NumPy, SciPy, pandas, scikit-learn, joblib, Pillow
CPRI circuit physics, diagnostics, fault scenarios and supported ML
4. Data & models
Local persistence
SQLite, SQLAlchemy, JSON, CSV / XLSX and joblib files
Saved runs, capture provenance, profiles and frozen model artifacts
Build & support
Local toolchain
Node.js, npm, PostCSS, pytest, HTTPX
openpyxl, Matplotlib, pypdf, PyYAML, XGBoost (optional)
03

## Slide 4
A COMPLETE RECOMMENDATION
CPRI example: a 1,425 kV lightning pulse
Generated circuit reference using assumed demo stock. Hardware suitability remains unverified.
04
Predicted waveform
Chart: Voltage (kV)
Setting | Value
Active stages | 11 of 12
Stage charge | 181.90 kV
Front R / stage | 30 Ω
Tail R / stage | 520 Ω
Stored energy | 22.75 kJ
Front 1.187 µs
Tail 53.74 µs
Charge solves the crest target.
Timing still differs from the target.

## Slide 5
BEYOND RECOMMENDATION
Waveform diagnostics and the digital twin
Conceptual circuit view. Briefing checkmarks never authorize physical high-voltage work.
05
Comparison workflow
Record what was fired
Save the actual settings and re-solve.
Upload and review
CSV or calibrated image, origin and quality.
Possible causes with uncertainty
Component shifts, measurement or model issues.
Conceptual assembly view
Stage C
Energy
Front R
Rise
Loop L
Ringing
Load C
Object
Tail R
Decay
Five virtual component groups
Inspect RLC values, place components digitally and review safety at each step.

## Slide 6
FAULT TEST LAB
Chopped impulses and generator stage failure
Generated scenarios at fixed original charge. Results depend on the stated fault topology.
06
Front and tail chopping
One stage fails to contribute
Chart: Voltage (kV)
Chart: Voltage (kV)
Front chop 1.06 µs
Tail chop 4.25 µs
Uncharged crest: 1,295.5 kV (−9.1%)
Bypassed crest: 1,312.3 kV (−7.9%)

## Slide 7
WHAT WE CAN DEMONSTRATE
Verification evidence and calibration results
07
Noiseless generated calibration study
Chart: Median absolute error (%)
| LI front | LI tail | LI crest | SI peak | SI tail | SI crest
Before fitting | 4.1012 | 0.85802 | 2.9195 | 3.7131 | 3.1487 | 4.0676
After fitting | 0.0058702 | 0.00077299 | 0.0014464 | 0.023953 | 0.004875 | 0.0030702
6 / 12 to 12 / 12 passing new setups
438 backend tests
28 frontend tests
36 / 36 expected outcomes
27 recommendations
9 expected rejections
7 / 7 fault gates
Independent numerical checks

## Slide 8
IMPULSETWIN AI
Conclusion
A working decision-support tool for
high-voltage impulse testing
Engineering value
Recommended settings come with
predicted waveforms and clear assumptions.
Extended capabilities
Waveform diagnostics, virtual assembly
and fixed-charge fault simulations.
Software checks and generated studies support the prototype.
Independent CPRI laboratory accuracy still needs validation.
Thank you
ImpulseTwin AI
08